Special-GOX

---
goal:
find xover operator for chromosomes, representing permutations with repetitions and variable length, which doesn’t produce illegal offspring
for chromosomes representing permutations with repetition could be used existing crossover GOX [1] (or some of it’s variants)
for permutations with repetition with variable length, I was not able to find such existing crossover

---
Generalized Order Xover
- input: 2 chromosomes as pwr (permutation with repetition)
- output: valid pwr child
- constraints:
  - number of each gene repetitions (for every gene)
    in both chromosomes must be the same
    => lengths of both chromosomes must equal
  - OK:	chr1 = A A B A B A C , chr2 = B C A A B A A
  - Not OK: chr1 = A A B A B A C , chr2 = B C A A B A B

---
0 3 2 0 1 5 0 6 0 7 0 9 8 0
GOX
0 3 5 6 0 1 0 2 0 7 0 9 8 0
1 1 1 2 1 1 3 1 4 1 5 1 1 6
0 3 2 0 1 | 5 0 6 0 7| 0 9 8 0
1.
0 3 5 | 5 0 6 0 7 | 6 0 1 0 2 0 7 0 9 8 0
0 3 x | 5 0 6 0 7 | x x 1 x 2 0 x 0 9 8 0
0 3 5 0 6 0 7 1 2 0 0 9 8 0
Two random cut points: indices 5, 9

---
proposed crossover operator for pwrvl
Idea: re-use known operators somehow
If two parent chromosomes differ in length:
  1. Shorten the longer chromosome
  2. Perform GOX
  3. Re-insert (somehow) the genes back to the child

---
- at random choose “non-essential” genes from chromosome
  (upper bound > 1 for presence in chromosome)
- calculate size of blocks between removed non-essentials (size of the blocks before merging)
- reinserting non-essentials:
  try to un-merge the blocks – to make the lengths after reinsertion as as close as possible to the ones before merging.

---
0 1 2 0 4 0 3 0 6 5 7 0 8 9 10 11 0
blocks
(1,2) → 3
(1,3) → 4
0 1 2 x 4 0 3 x 6 5 7 0 8 9 10 11 0
    0 1 2 4 0 3 6 5 7 0 8 9 10 11 0
GOX
Chromosome 2
 0 3 6 5 0 1 2 4 7 0 8 9 10 11 0
0 3 6 + 5 0 1 2 4 + 7 0 8 9 10 11 0
One possible reinsertion

---
references
[1] (GOX operator) https://citeseerx.ist.psu.edu/viewdoc/download?doi=10.1.1.487.9575&rep=rep1&type=pdf